## Slide 1
Interpretable Turbofan Degradation & Health Monitoring
NASA C-MAPSS Digital Twin | Multi-Task Classification, RUL Regression & TreeSHAP Attribution
Rahul Bansode, Shubham Vaidya, Gaurav Yadav, Mufeed Rajapkar | TODO_DEPARTMENT
1. OPERATIONAL CHALLENGE
Turbofan rotating components undergo continuous thermal and mechanical wear. Line maintenance requires discrete health triage before structural failure occurs. Scalar RUL predictions alone lack engineering root-cause explainability for line shop dispatch.
2. 3-STAGE LIFECYCLE
Healthy (Stage 0): RUL > 100 cycles Normal baseline operation; no maintenance intervention.
Degrading (Stage 1): 30 < RUL <= 100 cycles Active thermodynamic drift; schedule depot borescope inspection.
Critical (Stage 2): RUL <= 30 cycles Immediate risk; aircraft grounding & engine overhaul required.
3. TELEMETRY & STATIONS
• All 21 telemetry channels preserved (no arbitrary pruning). • Flat sensor analysis (CV < 1e-4): 9 flat in FD001, 7 in FD003, and 0 in FD002/FD004. • Stations: Fan/Inlet, LPC, HPC (core), Combustor, HPT, LPT, and Pressure Ratio (epr).
4. PROCESSING PIPELINE
Fig. 1. Dual-path architecture: single-cycle Random Forest snapshot classification and 50-cycle LSTM temporal window regression.
5. KEY EMPIRICAL FINDINGS
0.8197
LSTM 3-Stage Macro-F1 (vs 0.730 RF)
+21.0 Cyc
Median Lead-Time Advantage (80% Eng)
49.18%
HPC Subassembly SHAP Attribution
6. CRITICAL STAGE DETECTION
Fig. 2. Critical degradation class (RUL <= 30) F1 score comparison across benchmark sub-datasets.
7. RUL REGRESSION PERFORMANCE
Dataset | Engines | Capped RMSE | Capped MAE | NASA Score
FD001 | 100 | 15.07 | 10.68 | 493.1
FD002 | 259 | 74.86 | 62.78 | 468759.9
FD003 | 100 | 47.85 | 39.00 | 22149.4
FD004 | 248 | 77.51 | 65.50 | 509085.7
8. EXPLAINABILITY & LEAD TIME
Fig. 3. Subassembly TreeSHAP vs permutation attribution; lead-time delay distribution; top-10 sensor rankings.
9. DIGITAL TWIN DASHBOARD
Fig. 4. Interactive aerodynamic telemetry pins showing healthy baseline (left) vs critical redline threshold drift (right).
10. LIMITATIONS
• Synthetic Benchmark: NPSS thermodynamic simulation; not carrier flight telemetry.
• Multi-Regime Collapse: Macro-F1 degrades on FD002/FD004 without operating condition clustering.
• Isolation Forest False Alarms: Unsupervised anomaly score yields high false alarm rates on non-stationary drift.
• Computational Latency: Sequence windowing incurs higher memory footprint than snapshot evaluation.
11. FUTURE WORK
• Operating regime clustering (k-means flight condition partitioning) prior to sensor normalization. • Physics-guided neural networks enforcing thermodynamic work balances. • Attention-based temporal Transformers for multi-fault trajectory modeling.
12. REFERENCES & ARTIFACTS
[1] A. Saxena et al., PHM08, pp. 1–9, 2008.
[2] S. Hochreiter & J. Schmidhuber, Neural Comp., 1997.
[3] F. T. Liu, K. M. Ting, Z.-H. Zhou, ICDM, 2008.
[4] L. Breiman, Machine Learning, 2001.
[5] S. M. Lundberg & S.-I. Lee, NeurIPS, 2017.
Scan for GitHub Code, Data & Benchmarks (>= 60 mm size)